## Slide 1
State Machine & Per-State Control
GreenPinkCamera Injectable Teardown
Flexiv Rizon4 · 6-state FSM · primitive / Cartesian / joint-impedance control

## Slide 2
The Controller Has Two Layers
Describe every state with BOTH layers
Layer 1 — Flexiv RDK Control Mode
NRT_PRIMITIVE_EXECUTION
Runs Flexiv primitives: MovePTP, MoveL, MoveC, InsertComp, FloatingCartesian, Contact, GraspComp, ZeroFTSensor
NRT_CARTESIAN_MOTION_FORCE
Direct operational-space motion / force (grasp descent)
NRT_JOINT_IMPEDANCE
Joint hold: SendJointPosition + SetJointImpedance (park arm rigidly during gripper-only actions)
Layer 2 — Control Paradigm
the Force / Joint / Operational language
JOINT SPACE
MovePTP (planned in joint space, % vel scale), joint-impedance hold, the cap twist
OPERATIONAL / CARTESIAN
MoveL, MoveC — commanded in m/s
FORCE / COMPLIANCE
InsertComp, FloatingCartesian, Contact, GraspComp, Cartesian impedance, gripper force-target 80 N, vise close-to-force 5 kg

## Slide 3
The State Machine
6 states · transition guards make it a real FSM
Initialization
→
Module Localization
→
Pick Injectable
→
Load Injectable
→
Ultrasonic Cutting
→
Component Disassembly
Transition guards (from recipe safety gates)
→ enter vise area
Arduino busy=false, faulted=false, blade_on=false, homed
→ cut
vise CLOSED, robot clear, rotary ≈ 0
→ after cut
CUT_HEIGHT=DONE, blade_on=false, x=z=0
fault edge (any state)
→ STOP_ALL (fault handler)

## Slide 4
Controller Legend
Color code reused on every state slide
JOINT
NRT_JOINT_IMPEDANCE
Primitives:
MovePTP · joint hold · cap twist
OPERATIONAL
NRT_CARTESIAN_MOTION_FORCE
Primitives:
MoveL · MoveC (m/s)
FORCE / COMPLIANCE
force-aware primitives
Primitives:
InsertComp · FloatingCartesian · Contact · GraspComp · gripper 80 N · vise 5 kg

## Slide 5
State 1 — Initialization
Bring robot, gripper and machine to a known safe state
CONTROL:
Joint-space
Gripper
Primitive / action sequence
1. gripper open
2. MovePTP → Inter
3. MovePTP → Home
RDK control mode
NRT_PRIMITIVE_EXECUTION
Defining parameters
MOVE_JNT_VEL_SCALE = 80% · gripper 0.05 m/s

## Slide 6
State 2 — Module Localization
Re-localize the vise via ChArUco before any vise interaction
CONTROL:
Joint-space
Vision (no closed-loop force)
Primitive / action sequence
1. MovePTP → Vise-cali
2. ChArUco detect (cali tag 1/2/3)
3. reload Vise.json
4. MovePTP → Home
RDK control mode
NRT_PRIMITIVE_EXECUTION
Defining parameters
hand-eye camera_tcp.yaml · tag_01_to_vise_tcp.json

## Slide 7
State 3 — Pick Injectable
Camera-aligned approach + contact-guided adaptive grasp
CONTROL:
Operational
Force (contact grasp)
Primitive / action sequence
1. MovePTP → Plate
2. Align Injectable (MoveL)
3. ZeroFTSensor → Contact → GraspComp
4. MoveL lift +20 cm
RDK control mode
NRT_PRIMITIVE_EXECUTION + NRT_CARTESIAN_MOTION_FORCE
Defining parameters
align 0.02 m/s · contact 0.05 m/s · grip 80 N

## Slide 8
State 4 — Load Injectable
SHOWCASE STATE — cycles through all three RDK modes
CONTROL:
Force/compliance
→ Joint hold
→ Operational
Primitive / action sequence
1. MovePTP → above_vise
2. InsertComp (−Z → TCP X)
3. FloatingCartesian y/z/rx while vise → 5 kg
4. joint hold
5. gripper release
6. MoveL retreat
RDK control mode
ALL THREE: PRIMITIVE_EXECUTION · CARTESIAN_MOTION_FORCE · JOINT_IMPEDANCE
Defining parameters
INSERTCOMP_INSERT_VEL = 0.02 · maxContactForce · float maxVel 0.2 m/s

## Slide 9
State 5 — Ultrasonic Cutting
Machine cuts while robot waits clear; then grip + twist off cap
CONTROL:
Machine
Force-float
Joint-space twist
Primitive / action sequence
1. Arduino CUT_HEIGHT (robot idle/clear)
2. MoveL down
3. FloatingCartesian y/z/rx
4. gripper 80 N
5. twist about TCP X 0→+7→−10°
6. MoveL lift
RDK control mode
NRT_PRIMITIVE_EXECUTION
Defining parameters
CUT z=134.2, x=110.5, deg=360 · twist scale 20%

## Slide 10
State 6 — Component Disassembly
Fast-mode pick-and-place of spring, plastic, shell & glass
CONTROL:
Joint transit
Operational
Force-grip
Primitive / action sequence
1. MovePTP transit (×N)
2. MoveL descend / lift 0.5 m/s
3. gripper 80 N
4. Arduino OPEN_VISE
5. MoveC dump arc
RDK control mode
NRT_PRIMITIVE_EXECUTION
Defining parameters
FRAME5_CARTESIAN_VEL = 0.5 m/s · dump 0.03 m/s

## Slide 11
Two Things To Remember
1 · Color-code by control paradigm
Blue = joint, green = operational, red = force — consistent across the FSM and every state slide. Pick & Load read as force-rich; Disassembly is mostly kinematic.
2 · Load Injectable is the showcase state
It is the only state that cycles through all three RDK modes: compliant InsertComp → floating force → joint-impedance hold → Cartesian retreat. This is your 'we understand control architecture' slide.